## Slide 1
IOT BASED SMART IRRIGATION SYSTEM
‘
’
BY BARATH G (18BCA0083)
RUDRA GANESH R (18BCA0084)
SUDHARSUN M (18BCA0086)

## Slide 2
OVERVIEW
INTRODUCTION
MODULES
WATER LEVEL MONITORING
SOIL MOISTURE MONITORING
TEMPERATURE AND HUMIDITY MONITORING
RAIN MONITORING
TYPES OF IRRIGATION
ALERT SYSTEM OR ALARM SYSTEM
DATABASE & ANDROID APPLICATION
ADVANTAGES
CONCLUSION

## Slide 3
INTRODUCTION
The agricultural sector is one of the most important economic resources for many countries adding to the importance of managing well the available water resources using the well organized irrigation system
The Smart irrigation System has wide scope to automate the complete irrigation system. Here we are building a IoT based Irrigation System using ESP8266 NodeMCU Module and DHT11 Sensor. It will not only automatically irrigate the water based on the moisture level in the soil but also send the Data to Blynk Application to keep track of the land condition. The System will consist a water pump which will be used to sprinkle water on the land depending upon the land environmental condition such as Moisture, Temperature and Humidity.

## Slide 4
MODULES
WATER LEVEL MONITORING
SOIL MOISTURE MONITORING
TEMPERATURE AND HUMIDITY MONITORING
RAIN MONITORING
TYPES OF IRRIGATION
ALERT OR ALARM SYSTEM
DATABASE
ANDROID APPLICATION

## Slide 5
WATER LEVEL MONITORING
•This Module represents the water level monitoring system which helps to monitoring the water level of the tank or well without the use of man power.
•Very Effortless, human energy is not required.
•Low Efficient Cost.
•Farmer is not required to go around to the tank and check the availability of water is enough or not at anytime.
•It is very helpful for the Farmers.

## Slide 6
SOIL MOISTURE MONITORING
•This Module represents the soil moisture monitoring system which is very helpful to monitoring the moisture of the soil.
•Low Efficient Cost and cheap, also very Effortless.
•YL-69 Sensor is used to check the moisture level of soil.
•Very Useful for the Farmers and Nursery Gardeners.

## Slide 7
TEMPERATURE AND HUMIDITY MONITORING
• This Module represents the Temperature and Humidity monitoring system which is useful to monitor the Temperature and Humidity Level of Soil.
• DHT11 Sensor is Used to monitor the Temperature and Humidity level of soil.
• Low Cost, Very Useful and cheap in Market.
• Very helpful for Nowadays.
• User can check the Temperature and Humidity level at anywhere and anytime.

## Slide 8
RAIN MONITORING
This Module represents the Rain Monitoring with the use of Rain drop sensor.
Raindrop sensor is basically a board on which nickel is coated in the form of lines. It works on the principal of resistance.
Rain Sensor module allows to measure moisture via analog output pins and it provides a digital output when a threshold of moisture exceeds.
With the use of Rain drop sensor we sends the digital data to ESP8266 ,then ESP8266 send the data to Realtime database of firebase.
With the help of firebase our Android application shows the status of Rain.

## Slide 9
TYPES OF IRRIGATION
There are different types of irrigation practiced for improving crop yield. These types of irrigation systems are practiced based on the different types of soils, climates, crops and resources.
The main types of irrigation followed by farmers include:
Surface Irrigation:
In this system, no irrigation pump is involved. Here, water is distributed across the land by gravity.
Localized Irrigation:
In this system, water is applied to each plant through a network of pipes under low pressure.
Sprinkler Irrigation:
Water is distributed from a central location by overhead high-pressure sprinklers or from sprinklers from the moving platform.

## Slide 10
TYPES OF IRRIGATION
Drip Irrigation:
In this type, drops of water are delivered near the roots of the plants. This type of irrigation is rarely used as it requires more maintenance.
Centre Pivot Irrigation:
In this, the water is distributed by a sprinkler system moving in a circular pattern.
Sub Irrigation:
Water is distributed through a system of pumping stations gates, ditches and canals by raising the water table.
Manual Irrigation:
This a labour intensive and time-consuming system of irrigation. Here, the water is distributed through watering cans by manual labour

## Slide 11
ALERT OR ALARM SYSTEM
This Module represents the alarm system with the use of Buzzer.
Buzzers are used for making beeps, tones and alerts. To use, connect short pin to ground and the other pin to 5 voltage level.
User can set the alarm for the soil moisture ,temperature an humidity with the use of our Android Application.
Once you sets the alarm our application compares the sensor given data with user data ,If the sensor given data is less than or equal to user data buzzer will turn on.

## Slide 12
DATABASE
A database is a collection of information that is organized so that it can be easily accessed, managed and updated. In our Project we are using data base for storing and retrieving the sensor given values. We used ‘firebase’ to connect our project to database .
FIREBASE
The Firebase Realtime Database is a cloud-hosted database. Data is stored as JSON and synchronized in realtime to every connected client. When you build cross-platform apps with our iOS, Android, and JavaScript SDKs, all of your clients share one Realtime Database instance and automatically receive updates with the newest data.

## Slide 13
ANDROID APPLICATION
Android App is a software designed to run on an Android device or emulator. The term also refers to an APK file which stands for Android package. This file is a Zip archive containing app code, resources, and meta information. Android apps can be written in Kotlin, Java, and C++ and are run inside Virtual Machine
We created our own android application with the name of smart irrigation . Our app will show the current temperature and humidity and also soil moisture of the garden or agriculture field With the condition of soil like dry, damp and wet . And we have control of turning on and off of water pump from any part of the world.

## Slide 14
REQUIREMENTS
HARDWARE REQUIREMENTS
NODEMCU ESP8266
12V SOLENOID VALVE
SOIL MOISTURE YL-69 SENSOR
RAIN DROP SENSOR
TEMPRATURE & HUMIDITY DHT11 SENSOR
BREAD BOARD
JUMPER WIRES
SOFTWARE REQUIREMENT
ARDUINO IDE
ANDROID STUDIO
FIREBASE

## Slide 15
ADVANTAGES
Smart irrigation systems offer a variety of advantages over traditional irrigation systems. Smart irrigation systems can optimize water levels based on things such as soil moisture and weather predictions. This is done with wireless moisture sensors that communicate with the smart irrigation controls and help inform the system whether or not the landscape is in need of water. Additionally, the smart irrigation controlled receives local weather data that can help it determine when a landscape should be watered.
Rather than wasting water resources and your valuable money on watering your landscape you can take advantage of the nature moisture from the storm and save that water for another day when it is more needed. The advantages of these smart irrigation systems are wide reaching. The smart irrigation system will help you have better control of your landscape and irrigation needs as well as peace of mind that the smart system can make decisions independently if you are away

## Slide 16
ADVANTAGES
Additionally, we have all seen many places in the country that have experienced water scarcity and we know that our water resources are precious. With smart irrigation systems we can take better care of our resources which is better for the environment. The opportunity to save water, have better control and be more eco-friendly while maintaining landscape are just a few of the advantages a smart irrigation system provides and would make a wonderful addition to any home.

## Slide 17
CONCLUSION
The smart irrigation system implemented is cost effective for optimizing water resources for agricultural production. The proposed system can be used to switch on/off the water sprinkler depending on the soil moisture levels thereby making the process simpler to use. Through this project it can be concluded that there can be considerable development in irrigation with those of IOT and automation. Thus this system is a solution to the problems faced in the existing process of irrigation.